## Slide 1
Transceiver Performance What’s new in the last year?
Rob Sherwood
NCØB
Lots of options for your dollars.
Sherwood Engineering

## Slide 2
What is important in a contest environment?
Good Dynamic Range to hear weak signals in the presence of near-by strong signals.
You need a better receiver for CW than for SSB.
Be a good neighbor: i.e. Have a clean signal.
Transmitters continue to be a mixed bag.

## Slide 3
What Parameter is Most Important for a CW Contester?
Close-in Dynamic Range (DR3)
(We have to know the noise floor to calculate Dynamic Range)

## Slide 4
What is Noise Floor?
Sensitivity is a familiar number, normally applies to SSB.
Sensitivity = 10 dB Signal + Noise / Noise (10 dB S+N/N)
Noise Floor = 3 dB Signal + Noise / Noise (3 dB S+N/N)
Noise floor can be measured at any filter bandwidth, CW or SSB, for example, and is bandwidth dependent.
League normally only publishes noise floor for a CW bandwidth, typically 500 Hz CW filter.

## Slide 5
Noise Floor – Rarely an Issue on HF
On 20 meters and below, atmospheric, galactic and man-made noise predominates.
On 15 meters, in a quiet rural location, the receiver is still rarely the limit. Example:
NC0B, 5 element yagi at 70 feet, 270 feet of 7/8th inch hardline, antenna pointed in the quietest direction (30 degrees) at 4 PM on 2/28/2010.
Receiver sensitivity, no preamp, 2.4 kHz = 0.5 uV
Receiver sensitivity, w/ preamp, 2.4 kHz = 0.2 uV
Receiver noise floor, w/ preamp, 500 Hz = -135 dBm

## Slide 6
LJ-155CA yagi in the previous example

## Slide 7
A simple test with only a analog meter
Most hams don’t own a calibrated signal generator.
How do you evaluate your receiver?
Measure the noise gain when you connect your antenna.
All you need is an analog meter with a dB scale, hooked up to your speaker.

## Slide 8
Measure the noise gain
Disconnect your antenna and set the volume so your dB meter reads -10 dB.
(Put a dummy load on the rig, but it will likely make no difference.)
Connect the antenna and see how many dB the noise goes up when tuned to a dead spot on the band.
Do this with Preamp OFF and ON

## Slide 9
What did I measure on 15 meters ?
With preamp OFF, noise gain = 3.0 dB
With preamp ON, noise gain = 8.3 dB
(This was in the quietest direction!)
With the preamp ON, now rotate your yagi 360 degrees and note the difference in noise.
In the direction there is skip, the noise will be higher.
Can be a 10 dB difference in band noise vs. direction.

## Slide 10
15 & 10 meters not that different
Rig = IC-756 Pro III
10 meter antenna = Hy-gain 105CA @ 65 feet
15 meter antenna = Hy-gain 155CA @ 70 feet
Preamp 15 M 10 M
None 4 dB 3 dB
Preamp 1 11.5 dB 9.5 dB
Preamp 2 13.0 dB 11.0 dB

## Slide 11
More Variables – Plan ahead if you can
At my QTH there are two towers near the house and four 200 to 350 feet away. My noise level on 20 – 10 meters is vastly worse for the close-in towers, unless I turn off electronic devices.
TVs (CRT or plasma), UPS & family-room computer, broadband router (makes birdies), wireless Internet dish, wall warts with switching power supplies, hand touch lamp !

## Slide 12
Tower Distance vs. local RFI (noise)

## Slide 13
Noise Floor Quite Consistent in Top 10
FTdx-5000D -135 dBm
Elecraft K3 -138 dBm
Perseus -125 dBm (No preamp)
Flex 5000 -135 dBm
Orion II -133 dBm
Orion I -135 dBm
T-T Eagle -132 dBm
Flex 3000 -139 dBm
TS-590S -137 dBm
Icom R9500 -130 dBm
Drake R-4C -138 dBm (For comparison)
Numbers with Preamp-1 ON

## Slide 14
What is Dynamic Range?
The range in dB of very strong signals to very weak signals that the receiver can handle At The Same Time
What is Close-in Dynamic Range vs
Wide-Spaced Dynamic Range?
Why is Close-in Dynamic so important for CW ops?
Why is it less important for SSB operators?

## Slide 15
Third Order IMD to Measure Dynamic Range
Signal
Signal
IMD
IMD
2 kHz spacing
2 kHz spacing
2 kHz spacing

## Slide 16
Wide & Close Dynamic Range
20 kHz Spacing
2 kHz Spacing
First IF Filter at 70.455 MHz
IMD 20 kHz Away
15 kHz Wide
First IF Filter at 70.455 MHz
IMD 2 kHz Away
15 kHz Wide

## Slide 17
This keeps the undesired strong signals from progressing down stream to the next stages.
DSP
Filtering
SSB BW
Filter
Amplifier
Mixer
Mixer
CW BW
Filter
Highest performance with a bandwidth appropriate filter right up front after the first mixer.

## Slide 18
What has changed in last 8 years?
Ten-Tec started the change in 2003 with the Orion, the first radio to drop “up-conversion” and go back to a low first IF.
Elecraft followed, and now Yaesu and Kenwood in 2010.
Only Icom has of yet not offered a “down-conversion” radio
If the TS-590S is a big seller, will Kenwood follow on with a larger and more expensive model?

## Slide 19
When are 2 Out of Pass Band Signals a Problem?
If you know the close-in dynamic range of a radio, at what signal level will IMD start to be a problem?
S Meter standard is S9 = 50 V, which is –73 dBm
Assume a typical radio:  500 Hz CW filter  Noise Floor of -128 dBm  Preamp OFF
Dynamic Range Signal Level Causing IMD = Noise Floor
55 dB S9 FT-757 (56 dB)
60 dB S9 + 5 dB FT-2000 (61 dB)
65 dB S9 + 10 dB IC-7000 (63 dB)
70 dB Typical Up-conversion S9 + 15 dB 1000 MP / Mk V Field (68 / 69 dB)
75 dB S9 + 20 dB 756 Pro II / III (75 dB)
80 dB S9 + 25 dB Omni-VII / IC-7800 (80 dB)
85 dB S9 + 30 dB TS-590S (88 dB)
90 dB S9 + 35 dB Eagle & Flex 3K (90 dB)
95 dB S9 + 40 dB Orion II & Flex 5000A (95 dB)
100 dB S9 + 45 dB FTdx-5000, K3 (200 Hz roofing)

## Slide 20
Dynamic Range of Top 8 Transceivers
FTdx-5000D 101 dB
Flex 5000 96 dB (Flex users raise hand)
Elecraft K3 95 dB (with 500 Hz filter)
Orion II 95 dB
Orion I 93 dB
TT Eagle 90 dB
Flex 3000 90 dB
TS-590S 88 dB (Low Freq 1st IF mode)
TS-590S 76 dB (30, 17, 12, 10 & 6 M)
Close-in 2-kHz Test @ 500 Hz BW

## Slide 21
How did the new rigs perform on CW?
I used the FTdx-5000, TS-590S and Eagle in the 160 m. ARRL, Stew Perry & CQ contests.
Switched between the Kenwood and the Ten-Tec during the CQ contest.
Overload was never an issue.
All could crank down the DSP filter to 100 Hz or narrower.
Ran most of the contest at 200 Hz BW
Definitely needed 50 to 100 Hz BW

## Slide 22
Narrow DSP Filters Come Through
In all three contests working CE1/K7CA required the narrowest bandwidths to copy through the pile-up, since he was not working split.
Thank goodness the DXpeditions work split, so you can hear when the DX comes back to you.
You can imagine what it is like at the DX location: total pandemonium for days!

## Slide 23
The DR3 “window” is not fixed
The dynamic range of a radio is the same with an attenuator ON or OFF.
If on a noisy band, attenuate the noise and all signals to make better use of the dynamic range, and reduce the chance of overload.
If band noise goes from S6 to S2 by turning on the attenuator, you have lost nothing, yet your radio is being stressed much less.

## Slide 24
Let’s now look at the transmitters
I am now testing transmitters with white noise feeding the microphone, in addition to a two-tone test.
The effect of IMD products (splatter) are more obvious with noise.
Think of it as a 1000 tone test, more approximating real voice.

## Slide 25
White Noise Mk V Class A vs. K3 Class B @ 75 Watts
-60 dB
-60 dB
6 kHz
1.5 kHz
Courtesy W6XX

## Slide 26
What shipped since Dayton 2010?
Yaesu FTdx-5000D
Kenwood TS-590S
Ten-Tec Eagle

## Slide 27
Ten-Tec Eagle Class B White Noise
60 dB down 7 kHz away

## Slide 28
Kenwood 590S Class B White Noise
60 dB down 5 kHz away

## Slide 29
IC-7600 on top, 756 Pro III on bottom
7600 about 10 dB worse than the Pro III
8 dB Offset
18 dB difference at 6 kHz

## Slide 30
FTdx-5000D Class A – Two Levels ALC
No ALC
ALC Half Scale
60 dB down 2 kHz away

## Slide 31
What’s wrong with the FTdx-5000D?
Decades ago Collins clearly stated that an ALC circuit should have a SLOW time constant (decay). ALC should just be a slow leveling circuit. Speech processing should be done way before the PA and the ALC.
This issue can be fixed, either in hardware or in firmware, but I don’t know which it is.

## Slide 32
Ham breaks into my 20 meter QSO
When some breaks in to comment on your signal, what is your first thought?
“I must be splattering”
With the 5000D in Class A, and NO ALC, the ham broke in to say I had the cleanest signal he had ever seen on the air with his K3 and his P3 bandscope.

## Slide 33
What Could Contests Be Like?
What would CQ WW or ARRL DX be like if everyone had a signal this clean?
Yet some hams don’t want a clean signal.
They want “elbow room”.
This goes back to Contest Ethics from this morning!

## Slide 34
Back to CW signals
We have seen how width of an SSB signal & its IMD products affects how close you can operate to another station.
How does CW compare?
How close can we work to a strong adjacent CW signal?

## Slide 35
What is the Bandwidth of CW Signal?
On channel signal = S9 + 40 dB (-33 dBm)
Receiver = K3, 400 Hz 8-pole roofing + 400 Hz DSP Filter
Transmitter = Omni-VII with adjustable rise time
Undesired signal 700 Hz away, continuous “dits” at 30 wpm
Rise time of Omni-VII Strength of CW sidebands
Signal S9 + 40 -33 dBm Ref
3 msec S7 -83 dBm -50 dB
4 msec S6 -88 dBm
5 msec S6 -88 dBm
6 msec S5 -93 dBm 22 dB !
7 msec S4 -99 dBm
8 msec S4 -99 dBm
9 msec S4 -99 dBm
10 msec S3 -105 dBm -72 dB

## Slide 36
Spectrum of CW Signal on HP 3585A Analyzer
Rise Time 10 msec, “dits” at 30 WPM, Bandwidth -70 dB = +/- 450 Hz = 900 Hz

## Slide 37
Spectrum of CW Signal on HP 3585A Analyzer
Rise Time 3 msec, “dits” at 30 WPM, Bandwidth -70 dB = +/- 750 Hz = 1500 Hz

## Slide 38
Spectrum of CW Signal on HP 3585A Analyzer
Comparison of 3 msec vs 10 msec rise time
20 dB difference

## Slide 39
Leading edge of “dit” 3 & 10 msec

## Slide 40
On SSB you want DR3 = 70 dB, or more. On CW you want DR3 = 80 dB, or more. This is most economically accomplished with low IF (5 to 9 MHz) selectable crystal roofing filters. It is much more difficult to deliver 80 dB or higher DR3 with the more common Up-Conversion design. Transmitted bandwidth of the interfering signal is often the limit, not the receiver.
Just the Facts

## Slide 41
80 dB or better @ 2 kHz with a 500 Hz bandwidth.
2001 Ten-Tec Omni-VI+: 80 dB
2003 Icom IC-7800: 80 dB
2003 Ten-Tec Orion I: 93 dB
2005 Ten-Tec Orion II: 95 dB
2007 Flex 5000A: 96 dB
2007 Ten-Tec Omni-VII: 80 dB
2008 Elecraft K3: 95 dB
2010 Kenwood TS-590S: 88 dB
2010 Ten-Tec Eagle: 90 dB
2010 FTdx-5000: 101 dB
What dynamic range is possible and needed for CW?

## Slide 42
Elecraft K2: 80 dB
Collins R-390A: 79 dB
Kenwood TS-850S: 77 dB
Icom Pro II / Pro III 75 dB
Collins 75S-3B/C: 72 dB
Kenwood TS-870S: 69 dB
Yaesu FT-2000: 63 dB This is shockingly bad
Icom IC-7000: 63 dB
Yaesu FT-One: 63 dB
Yaesu FT-101E: 59 dB
Drake R-4C Stock: 58 dB
Yaesu FT-757: 56 dB
Yaesu VR-5000: 49 dB Worst radio I have ever tested !
Other radios for comparison, 2 kHz dynamic range data

## Slide 43
Bogus ARRL Dynamic Range Numbers
Many modern transceivers are phase noise limited, particularly close-in at 2 kHz. The League wanted be able to measure the IMD buried in the phase noise, and came up with a new method a few years ago using a spectrum analyzer with a 3-Hz filter.

## Slide 44
IC-7600 with 3-Hz Spectrum Analyzer
Phase noise limited dynamic range is 78 dB at 2 kHz.
Measured with a 3-Hz filter on the analyzer, the dynamic range is 87 dB at 2 kHz!
IMD @ -130 dBm
Reference tone -130 dBm
500 Hz DSP Filter Passband

## Slide 45
What the New ARRL DR3 Method Means
Old method, IMD or noise increased 3 dB.
IMD tone at noise floor =
This was DR3, either IMD or noise limited.
With the new method, noise increased 10 dB, and by ear you hear nothing but noise.
How is this the same?
Unless you work a contest using a 3-Hz CW filter, the new League dynamic range measurements are meaningless. If the radio is phase noise limited.

## Slide 46
IC-7800 ARRL Old vs. New Method
4/18/2006 IC-7800 test data, old method
2 kHz, Phase Noise Limited @ 80 dB
1 kHz, Phase Noise Limited @ 67 dB
2/6/2007 IC-7800 test data, new method
2 kHz, dynamic range = 86 dB
No measurement reported at 1 kHz.

## Slide 47
Flex 3000 Old Method vs. 3 Hz Filter
Flex 3000 with Old Method: DR3 = 90 and is completely phase noise limited.
Flex 3000 with 3 Hz Spectrum Analyzer method measures a dynamic range between 95 and 99 dB, depending on the spacing.
The Orion II and the K3 perform better, but now you cannot tell that by the QST numbers.

## Slide 48
Phase noise should not be ignored !
The problem is the League is now measuring dynamic range in such a way to eliminate phase noise from the equation. Phase noise (reciprocal mixing in a QST review) gets but a single line of data.
An Elecraft K3 at 99 dB is not the same as a Flex 3000 at 99 dB, yet you would never know that from a QST review.

## Slide 49
Question: How good is good enough?
High Dynamic Range Receiver (DR3).
Minimum 70 dB for SSB & 80 dB for CW
If the “real” DR3 > 90 dB, your receiver is fine.
Differences of a few dB are NOT significant.
Sensitivity 15 meters and below, preamp ON: 0.2 uV
Noise floor 15 meters and below, preamp ON: -135 dBm
Receiver testing needs to approximate the real world.

## Slide 50
Sherwood Engineering
http://www.sherwood-engineering.com
http://www.NC0B.com