## Slide 1
Ground Screen Replace / Compliment a Radial System
Rob Sherwood
NCØB
We don’t all have space for a 200 x 200 foot ground system = 0.9 acres.
Sherwood Engineering

## Slide 2
My First House & Antenna
Purchased house in 1971
No money for a tower
Put up 48 foot vertical on side of house
Lot size is only 62 x 120 feet
Installed six 25 to 40-foot radials in semicircle.
Antenna barely worked & I had RF in the shack !

## Slide 3
On 80 meters the resistive value of a 48 foot vertical with a decent ground system would be 15 to 20 ohms.
With 6 short radials the R was over 100 ohms.
Laid down a 3 x 30 foot strip of hardware mesh.
The antenna now tuned with a reasonable R value. This was my only antenna for 1 year.
Time to make some quantitative measurements.

## Slide 4
1977
Test Setup
36 foot vertical, chicken wire ground screen, GR RF bridge, sig gen and receiver.

## Slide 5
Measurements on a 36-Foot Vertical
Data from my May 1977 hr magazine article.
General Radio 916A RF Bridge
Best numbers with ground screen in an X
45x2 feet + 25x5 feet at 90 degrees
200 square feet of screen
1.8 MHz Z = 8 ohms –j717.
3.6 MHz Z = 15 ohms –j279
All the data is on my web site: www.nc0b.com

## Slide 7
Jump ahead 30 years to new QTH
Marconi T antenna
600+ Square Feet of Ground Screen
(Dip galvanized hardware cloth / mesh)
Screen layout in an X at 90 degrees

## Slide 8
Ground Screen in Back Yard

## Slide 9
Closer Shot of Screen

## Slide 10
160 Meter T Antenna
150 or 200 foot flattop strung between two towers
Could use trees or poles
(If one support, flattop wires can angle down)
Vertical downlead attached in the middle of flattop
Vertical section is 60 feet long
Redesign for 80 meters, it could be half this size.
Most hams can string 75 feet of wire 30 feet in the air.

## Slide 11
Measurements with GR RF Bridge
Initial 200 foot flattop data:
1.8 MHz 36 ohms + j310
1.9 MHz 44 ohms + j363
2.0 MHz 49 ohms + j427
Now add 20 100-foot radials to see how much improvement
1.8 MHz 28 ohms + j305
1.9 MHz 36 ohms + j368
2.0 MHz 42 ohms + j438
The Z of the antenna was reduced by 8 ohms
Note: 200 foot dipole lying on the ground resonant 1.9 MHz

## Slide 12
Shortened flattop from 200 feet to 150 feet
150 foot flattop data with ground screen and 20 100 foot radials:
1.8 MHz 24 ohms +j161 (R value dropped 4 ohms)
1.9 MHz 29 ohms +j210 (R value dropped 7 ohms)
2.0 MHz 32 ohms +j262 (R value dropped 10 ohms)
Now add 20 more radials for a total of 40 100 foot radials
1.8 MHz 22 ohms +j161 (R value dropped 2 more ohms)
1.9 MHz 27 ohms + j210 The radials did make up
2.0 MHz 30 ohms +j262 for shortening the flattop.
The Z of the antenna decrease an additional 2 ohms
Decreased the impedance of the antenna 10 ohms with 4000 feet of wire compared to just 600+ square feet of ground screen.

## Slide 13
When is the antenna good enough?
On 160 meters I regularly worked JAs from CO with just the ground screen & 200 ft flattop.
The screen went 25 feet in 4 directions.
100 to 650 square feet of screen have been used over the years at four different QTHs, depending on my yard size.
I picked up about 1 dB with 4000 feet of radial wire. (This value determined later.)

## Slide 14
Tweaking the Antenna
What is the optimum flattop length with a 60 foot vertical?
I ran this by ON4UN who said:
“The ideal length for your T would be the length where the average current in the vertical would be highest, in other words where the current maximum would be about half way up the vertical section (30 ft).”
He modeled vertical wire of 60 ft and a top hat of 75 ft per side, and assuming a 5 Ohm ground loss resistance:
Modeled ON4UN: 1850 kHz = 27.7 +j190 ohms (5 ohm gnd)
Modeled W6XX: 1825 kHz = 27.7 +j190 ohms (20 radials)
Measured: 1850 kHz = 27 +j184 ohms
(screen + 20 radials)

## Slide 15
Field Strength Measurements
The pattern is almost perfectly circular on 160.
Frequency Field Strength (mV/M)
Theoretical 186 mV/M @ 1 mile @ 1 kW
Typical @ 1.6 MHz 165 mV/M, good soil (-1.0 dB)
KRXY @ 1.6 MHz 160 mV/M (-1.3 dB)
NC0B @ 1.9 MHz 130 mV/M (-3.1 dB)
W7KKD @ 1.8 MHz 110 mV/M * (-4.6 dB)
* (50-foot vertical, 20-foot top loading hat & 12 radials)

## Slide 16
Efficiency with 150 foot flattop @ 1 Mile
40 Radials + Ground Screen Z = 27 ohms
Theoretical Measured Difference
186 mV/M 130 mV/M (-3.1 dB)
@ 400 & 800 feet NEC implies ground losses 7 ohms
20 Radials + Ground Screen Z = 29 ohms
Extrapolate 125 mV/M (-3.5 dB)
Increase ground losses to 9 ohms
Adding 20 radials improved signal 0.4 dB

## Slide 17
Calculated watts in vertical section
150 foot & 40 radials + screen 741 W Reference
150 foot & 20 radials + screen 690 W -0.31 dB
200 foot & 20 radials + screen 750 W +0.05 dB
200 foot & screen only 614 W -0.87 dB
10 Log Power1/Power2 = dB
If you don’t have an acre of ground and almost a mile of wire, you can compete by using just a ground screen and a reasonable size top-loaded vertical.

## Slide 18
Reality Check – Are Numbers reasonable?
Paper from NAB 1996, Kintronic Labs, Inc. measurements at Bluff City, TN.
0.27* wave tower, 120 radials, 1680 kHz, Ref
Ground stake only, signal level -2.7 dB
0.17^ wave tower, 120 radials, -1.4 dB
Ground stake only, signal level -5.2 dB
* 150 feet
^ 95 feet

## Slide 19
Radiation Pattern courtesy W6XX
160 meter peak radiation near 30 degrees.
1 dB down at 15 degrees above the horizon.
Note: Not a cloud warmer, down 10 dB at 75 degrees above the horizon.

## Slide 20
Horizontal dipole @ 1/8th wave length
Horizontal is efficient.
Favors short skip, making DX weaker by comparison to state-side QRM.
10 dB down at 15 degrees.

## Slide 21
Radiation Pattern 160 Meters by W6XX
Red = Horizontal
Down 29 dB or more from the vertical radiation pattern.

## Slide 22
How does it work on 80 meters?
Red = Horizontal
Down 10 dB or more from the vertical radiation pattern.
If the antenna is scaled to 80 meters, then it is a perfectly good antenna on 80 & 40 meters.

## Slide 23
Field Strength on 80 Meters
Voltage fed: 2400 ohms + j4000 !
Field Strength @ 1 mile & 1 kW
80 mV/meter in line with flattop
45 mV/meter 90 degrees to flattop
More groundwave loss on 80 vs. 160 meters.

## Slide 24
Radial Field Strength 400/800/1200 Ft – W6XX

## Slide 25
Radial Field Strength 1 to 20 Miles - W6XX

## Slide 26
Summary
What’s practical for your QTH?
Ground screen better than a few radials.
Broadcasters use a screen + radials.
Limited space? Use a ground screen.
How much? Shoot for 400 square feet.
Don’t recommend less than 100 sq ft.
Add radials? 16 or more, or don’t bother.
4 radials do virtually nothing.

## Slide 27
Sherwood Engineering
http://www.NC0B.com
Thanks to W6XX and K0ELM for their invaluable assistance