## Slide 1
Roofing Filters, Transmitted IMD and Receiver Performance
Rob Sherwood
NCØB
What’s important when it comes to choosing a radio?
Sherwood Engineering

## Slide 2
Why Did I Start Testing Radios ?
Purchased a new Drake R-4C in 1975
Used it during the ARRL 160m CW contest
Radio performed miserably, yet Specs Were Good
70s: League expanded testing to include Noise Floor & Dynamic Range, new concepts for the amateur.
R-4C tested well for Dynamic Range, but flunked CW contest 101.
Was the wrong thing being tested or did the test not approximate a real amateur environment, especially a CW contest environment?

## Slide 3
20 kHz Dynamic Range test showed that in a multi-conversion radio, it was only testing the radio’s front end.
If the first IF was 6 - 20 kHz wide, be it at 5 MHz, 9 MHz or 45 - 70 MHz, the radio would overload in a CW pile up.
20 kHz test showed no hint of the problem
Solution: Place test signals close together so they pass through 1st IF Filter  the Next Amplifier  Mixer
Close-in dynamic range numbers are ALWAYS worse than the wide-spaced numbers, for a radio with a single wide roofing filter.

## Slide 4
What 2 Numbers are Most Important for a CW Contester?
Noise Floor
Close-in Dynamic Range

## Slide 5
What is Noise Floor?
Sensitivity is a familiar number, normally applies to SSB.
Sensitivity = 10 dB Signal + Noise / Noise (10 dB S+N/N)
Noise Floor = 3 dB Signal + Noise / Noise (3 dB S+N/N)
Noise floor can be measured at any filter bandwidth, CW or SSB, for example.
League normally only publishes noise floor for a CW bandwidth, typically 500 Hz CW filter.

## Slide 6
What is Dynamic Range?
What is Close-in Dynamic Range vs. Wide-Spaced Dynamic Range?
Why is Close-in Dynamic so important for CW ops?
Why is it less important for SSB operators?

## Slide 7
Third Order IMD
Signal
Signal
IMD
IMD

## Slide 8
This keeps the undesired strong signals from progressing down stream to the next stages
Filter
500 Hz
Wide
Filter
6–12 kHz
Wide
Amplifier
Mixer
Mixer
Filter
600 Hz
Wide
What if we could switch in a narrow Roofing Filter only slightly wider than the final selectivity?

## Slide 9
Wide & Close Dynamic Range
20 kHz Spacing
2 kHz Spacing
First IF Filter at 70.455 MHz
IMD 20 kHz Away
12 kHz Wide
First IF Filter at 70.455 MHz
IMD 2 kHz Away
12 kHz Wide

## Slide 10
When are 2 Out of Pass Band Signals a Problem?
If you know the close-in dynamic range of a radio, at what signal level will IMD start to be a problem?
Assume S9 = 50 V which is –73 dBm
Assume a typical radio:  500 Hz CW filter  Noise Floor of -128 dBm  Preamp OFF
Dynamic Range Signal Level Causing IMD = Noise Floor
55 dB S9
60 dB S9 + 5 dB
65 dB S9 + 10 dB
70 dB S9 + 15 dB
75 dB S9 + 20 dB
80 dB S9 + 25 dB
85 dB S9 + 30 dB
90 dB S9 + 35 dB
95 dB S9 + 40 dB
100 dB S9 + 45 dB

## Slide 11
Transmitted IMD Collins 32S-3

## Slide 12
Compare the Old vs. New
Order Collins Yaesu Difference
IMD 32S-3 FT-450 in dB
3rd -39 dB -30 dB 9 dB
5th -49 dB -37 dB 12 dB
7th -59 dB -42 dB 17 dB
9th -68 dB -48 dB 20 dB

## Slide 13
Close-in Signal and Splatter
IF Filter vs. Adjacent Signal and IMD Splatter
Signal 5 kHz Away

## Slide 14: How Many Roofing Filters are Needed?
It depends on your mode of operation.
For SSB, a single 15 kHz roofing filter is adequate, such as in the Icom 756 Pro II / Pro III with a close-in dynamic range of 75 dB.
Other radios, old and new with similar performance: Drake R7/TR7, Collins 75S-3B/C, Icom 781, TS-830/930, FT-1000X, T-T Omni-V
Would a 3 kHz roofing filter be better? Yes, a fairly new concept.
On CW, a single wide roofing filter is not adequate.
CW signals do not have IMD products, thus strong adjacent signals do not have much energy in the CW passband of your filter.
(Some key click and phase-noise energy may be heard.)

## Slide 15: Conclusions
Contesters – DXers – Pileup operators need the best receiver possible, especially for CW operation
The Sherwood 600 Hz CW roofing filter fixed the R-4C in 1976, and the Ten-Tec Orion put that concept in a commercial design in 2003. Now the Elecraft K3 also offers multiple roofing filters of AM, SSB & CW bandwidths.

## Slide 16
25 years of up conversion radios have generally offered a 20 kHz dynamic range in the 90s but a 2 kHz close-in dynamic range in the 70s. Typical degradation of dynamic range within the up conversion filter bandwidth is 25 dB.
Now the buzz word is a 3-kHz roofing filter in up-conversion radios, though some are pure hype.
IC-7800 3-kHz filter is 5+ kHz wide. FT-2000 3-kHz filter is 7 kHz wide, with worse IMD than its 6 kHz filter.

## Slide 17
It is not possible to offer CW bandwidth Roofing Filters at VHF (up-conversion) frequencies.
The Orion II and the K3 roofing filters are in the 8 to 9 MHz range, similar to the R-4C at 5 MHz.
The only radios with no roofing filters at all are from Flex, like the 5000A. It basically converts everything to audio and filters it in DSP.

## Slide 18
What dynamic range is possible and needed for CW?
80 dB or better @ 2 kHz.
1976 Sherwood / Drake R-4C: 84 dB
2001 Ten-Tec Omni-VI+: 80 dB
2005 Ten-Tec Orion II: 95 dB
2007 Flex 5000A: 96 dB
2007 Ten-Tec Omni-VII: 80 dB
2008 Elecraft K3: 101 dB (with 200 Hz roofing filter)

## Slide 19
Other radios for comparison, 2 kHz data:
Kenwood TS-850S: 77 dB
Collins 75S-3B/C: 72 dB
Kenwood TS-870S: 69 dB
Yaesu FT-2000: 63 dB
Icom IC-7000: 63 dB
Yaesu FT-One: 63 dB
Yaesu FT-101E: 59 dB
Drake R-4C Stock: 58 dB
Yaesu FT-757: 56 dB
Yaesu VR-5000: 49 dB

## Slide 20
Sherwood Engineering
http://www.sherwood-engineering.com
http://www.NC0B.com