## Slide 1
DSP Radios Not Perfect
Rob Sherwood
NCØB
Dayton Drake Forum 2007
Sherwood Engineering

## Slide 2
Should you throw away your vintage radio ?
Yahoo Icom reflector moderator says “yes.”
See what you think in a few minutes.

## Slide 3
Since you are here, you likely own a classic Drake radio from the 70s and 80s.
In the past years I have given talks on:
Dynamic Range
Receiver Testing
Performance in Contest Environments

## Slide 4
Today I am going to discuss a more subtle problem.
Your Drake radios don’t have the problem.
Radios designed 10 years ago don’t have the problem.
Many hams are not catching on, and I don’t know why.
The ARRL testing lab is missing it completely.

## Slide 5
What is the problem?
All new DSP designs in the past 3 years have AGC problems.
At least one new design “folds up” in QRN.
Lab testing is important BUT
You have to LISTEN to radios, too.
Why are serious problems getting past R&D?

## Slide 6
Fall of 2005
Listening to weak signals on 20 m. with a new DSP radio
Hearing annoying clicks, ticks, and pops
Switched to R-4C – No clicks, ticks or pops at all
20-year-old Icom – No clicks, ticks, or pops
S-Line – No clicks, ticks, or pops

## Slide 7
The Problem
All new IF DSP radios from all manufacturers have the same
AGC problem on Fast Rise-Time Transients.

## Slide 8
Wave files
Normal Speech
Speech with AGC Interruptions

## Slide 9
Edited description of AGC in new K3 from Elecraft web site
“Will the settings allow the AGC to be set up to tolerate very fast rise-time waveforms while responding [properly] to [normal signals]?”
It goes on to say the blanker can eliminate pops if they are a problem.
You don’t even notice the pops on older radios since they don’t false trigger the AGC.
I can’t wait to listen to the K3 to see if they got it right.

## Slide 10
Older hybrid designs do not exhibit these bad AGC characteristics.
Icom 756 Pro, Pro II and Pro III are fine.
Fast rise transients are stretched by the IF filtering to 1 millisecond.
An R-4C has an R & C in the AGC.
A 1 msec transient cannot charge up the C.

## Slide 11
New AGC designs in DSP radios strongly react to the transients.
A “tick” may kick the S meter to S9 on newly designed radios.
The same “tick” does not even move an
R-4C S meter.

## Slide 12
Another new DSP problem
March, 2006, sold two 706MkIIGs
Bought new IC-7000.
Human interface is great. Easy to program.
Has same AGC problem + a different problem.

## Slide 13
IC-7000
Performs poorly in broadband noise, like QRN
Mobile trip KS to CO
40 meter CW, occasional QRN = S9
Wearing phones, QRN very wide band
Crashes way outside the 500 Hz CW passband
How to prove what I was hearing with my ears?

## Slide 14
HP 3561A FFT Analyzer
Swept vs FFT Analyzers

## Slide 15
R-4C
781
706
7000

## Slide 16
R-4C
R-4C
7000
781
706
QRN

## Slide 17
R-4C
781
706
7000
Single Tone

## Slide 18
How to Approximate Broadband Noise
Used 3 tone test to approximate broadband QRN.

## Slide 19
R-4C
706
7000
3 Tone
781

## Slide 20
Where does that leave us?
New IF DSP designs seriously exaggerate transient noise on weak signals.
Some DSP radios make QRN much worse.
Same problem on unblankable line noise.

## Slide 21
Are R&D Departments comparing old designs to new designs?
Some hams are noticing what I am describing, but many are not.
Maybe some hams may have sold all their older radios and cannot compare.
The bands are not always as noisy as the latest digital receivers make them appear.
An individual radio can make noise worse.

## Slide 22
Are you ready to sell your Drake?
Maybe NOT!

## Slide 23
Sherwood Engineering
www.sherwood-engineering.com
www.NC0B.com