## Slide 1
Roofing Filters, Transmitted BW and Receiver Performance
Rob Sherwood
NCØB
What’s important when it comes to choosing a radio?
Sherwood Engineering

## Slide 2
Why Did I Start Testing Radios ?
Purchased a new Drake R-4C in 1972
Used it during the ARRL 160m CW contest
Radio performed miserably, yet Specs Were Good
1970s: League expanded testing to include Noise Floor & Dynamic Range, new concepts for the amateur.
R-4C tested well for Dynamic Range, but flunked CW contest 101.
The ARRL dynamic range test did not approximate a real-world environment, especially in a CW contest.

## Slide 3
Dynamic Range - measures the ability to hear weak signals in the present of near-by strong signals.
A 20 kHz Dynamic Range measurement in a multi-conversion radio only tests the radio’s front end.
If the first IF was 6 - 20 kHz wide, be it at 5 MHz, 9 MHz or 45 - 70 MHz, the radio could overload in a CW pile up.
20 kHz dynamic range test showed no hint of the problem
Solution: Place test signals close together so they pass through 1st IF Filter  the Next Amplifier  Mixer
Close-in dynamic range numbers are ALWAYS worse than the wide-spaced numbers, for a radio with a single wide roofing filter.

## Slide 4
Considerations in Choosing a Transceiver
High close-in dynamic range (copy S1 in crowded band)
Low noise floor (copy very weak signals)
Low phase noise (low noise on the Local Oscillator)
Low in-band spurious on both receive and transmit
Low IMD on SSB transmit, and low key clicks on CW transmit
Effective SSB speech processor (more talk power)
Good receive and transmit audio quality (intelligibility)
Smooth AGC for low fatigue (noise doesn’t fill in spaces)
AGC that doesn’t exaggerate impulse noise (hangs up AGC)
Good ergonomics of controls and menus (easy adjustments)
Good display that also shows important settings

## Slide 5
What 2 Numbers are Most Important for a CW Contester?
Noise Floor
Close-in Dynamic Range (DR3)
(Noise floor need to calculate DR3)

## Slide 6
What is Noise Floor?
Sensitivity is a familiar number, normally applies to SSB.
Sensitivity = 10 dB Signal + Noise / Noise (10 dB S+N/N)
Noise Floor = 3 dB Signal + Noise / Noise (3 dB S+N/N)
Noise floor can be measured at any filter bandwidth, CW or SSB, for example, and is bandwidth dependent.
League normally only publishes noise floor for a CW bandwidth, typically 500 Hz CW filter.

## Slide 7
Third Order IMD
Signal
Signal
IMD
IMD
2 kHz spacing
2 kHz spacing
2 kHz spacing

## Slide 8
What is Dynamic Range?
The range in dB of very strong signals to very weak signals that the receiver can handle At The Same Time
What is Close-in Dynamic Range vs
Wide-Spaced Dynamic Range?
Why is Close-in Dynamic so important for CW ops?
Why is it less important for SSB operators?

## Slide 9
Wide & Close Dynamic Range
20 kHz Spacing
2 kHz Spacing
First IF Filter at 70.455 MHz
IMD 20 kHz Away
15 kHz Wide
First IF Filter at 70.455 MHz
IMD 2 kHz Away
15 kHz Wide

## Slide 10
This keeps the undesired strong signals from progressing down stream to the next stages
Filter
500 Hz
Wide
Filter
6–15 kHz
Wide
Amplifier
Mixer
Mixer
Filter
600 Hz
Wide
What if we could switch in a narrow Roofing Filter only slightly wider than the final selectivity?

## Slide 11
When are 2 Out of Pass Band Signals a Problem?
If you know the close-in dynamic range of a radio, at what signal level will IMD start to be a problem?
S Meter standard is S9 = 50 V, which is –73 dBm
Assume a typical radio:  500 Hz CW filter  Noise Floor of -128 dBm  Preamp OFF
Dynamic Range Signal Level Causing IMD = Noise Floor
55 dB S9 FT-757
60 dB S9 + 5 dB FT-101E
65 dB S9 + 10 dB KWM-380
70 dB S9 + 15 dB TS-830
75 dB S9 + 20 dB 756 Pro II / III
80 dB S9 + 25 dB Omni-VII
85 dB S9 + 30 dB R9500
90 dB S9 + 35 dB Orion I (93 dB)
95 dB S9 + 40 dB Orion II & Flex 5000A
100 dB S9 + 45 dB K3 (95 to 101 dB)

## Slide 12
The DR3 “window” is not fixed
The dynamic range of a radio is the same with an attenuator ON or OFF.
If on a noisy band, attenuate the noise and all signals to make better use of the dynamic range, and reduce the chance of overload.
If band noise goes from S6 to S2 by turning on the attenuator, you have lost nothing, yet your radio is being stressed much less.

## Slide 13
A Comment on IP3 (3rd Order Intercept)
I don’t publish IP3. It is a theoretical number.
It has more meaning for a block amplifier or mixer.
Almost meaningless if the AGC of a receiver is involved
October 2007 QST Product Review FT-2000D
DR3 Spacing Level IP3
98 dB 20 kHz Noise Floor +25 dBm
69 dB 2 kHz Noise Floor -19 dBm
29 dB 2 kHz 0 dBm = S9+73 dB +15 dBm

## Slide 14
Attenuators, Preamps & IP3
Dynamic range is constant if you enable an attenuator and often constant even with preamp enabled. IP3 varies all over the map. Data from March QST 2008 FT-950
Gain Dynamic Range IP3 dBm
Pre 2 95 +4 (published)
Pre 1 95 +13 (published)
No Preamp 94 +22 (published)
Att 6 dB 94 +28 (calculated)
Att 12 dB 94 +34 (calculated)
Att 18 dB 94 +40 (calculated)

## Slide 15
Comments on Blocking & Phase Noise
Blocking is the onset of gain compression.
This can be an issue with another ham within “line-of-site”.
It is an issue on Field Day and multi-multi contest stations.
Low phase noise is desirable, but a very good low phase-noise receiver has to contend with transmitted phase noise.
Dealing with transmitted phase noise is like dealing with transmitted IMD products and splatter.
We cannot do much about it.

## Slide 16
Lets now move from CW to SSB
Why are the dynamic range requirements less stringent on SSB than on CW?

## Slide 17
Transmitted IMD Collins 32S-3
-36 dB

## Slide 18
-27 dB
Solid-State Transceiver on 20 meters

## Slide 19
Yaesu FT-1000 Mk V in Class A
Provided by Pete, W6XX
-42 dB

## Slide 20
Mk V Class A + 8877 Linear Amplifier
-40 dB

## Slide 21
Compare the Old vs. New
Order Collins Yaesu Difference
IMD 32S-3 FT-450 in dB
QST
3rd -42 dB -30 dB 12 dB
5th -53 dB -37 dB 16 dB
7th -66 dB -42 dB 24 dB (Note)
9th -77 dB -48 dB 29 dB

## Slide 22
Close-in Signal and Splatter
IF Filter vs. Adjacent Signal and IMD Splatter
Signal 5 kHz Away
-60 dB, 7th Order

## Slide 23
Steady-State vs. Dynamic Splatter
Some transceivers, in addition to normal IMD products, produce additional ALC-Induced splatter. On CW the ALC can cause leading-edge key clicks.
ALCs could be driven hard in a 32S-3 or a T-4XC, for example, and not add to splatter.
Some modern rigs splatter more if the ALC is more than “tickled”, or induce clicks on CW.
The League has chosen not to address this problem in its equipment reviews. SM5BSZ & I tried to no avail.

## Slide 24: How Many Roofing Filters are Needed?
It depends on your mode of operation.
For SSB, a single 15 kHz roofing filter is adequate, such as in the Icom 756 Pro II / Pro III with a close-in dynamic range of 75 dB.
Other radios with similar performance: Drake R7 and TR7, IC-781, Collins 75S-3B/C, TS-930, FT-1000x, T-T Omni-V or VI.
Would a 2.7 kHz roofing filter be better?
Yes, K3, Orion, Omni-VII or non-DSP Hilberling PT-8000A.
On CW, a single wide roofing filter is not optimum.
CW signals do not have IMD products. Strong adjacent signals do not have as much energy in the CW passband of your filter.
A CW Signal Does have a Bandwidth. It is NOT zero bandwidth

## Slide 25
Roofing Filter BW on SSB
Do you need more than one SSB BW Filter?
Best if Roofing & DSP bandwidths are equal.
More selectivity up front is always desirable.
Better shape factor than depending of last IF only.
Omni-VII the 455 kHz filters really help total selectivity.
Orion & K3 both offer a 1.8 kHz roofing filter.
Reduces load on DSP !
Just not as dramatic improvement as on CW.

## Slide 26
Back to CW signals
We have seen how width of an SSB signal & its IMD products affects how close you can operate to another station.
How does CW compare?
How close can we work to a strong adjacent CW signal?

## Slide 27
What is the Bandwidth of CW Signal?
On channel signal = S9 + 40 dB (-33 dBm)
Receiver = K3, 400 Hz 8-pole roofing + 400 Hz DSP Filter
Transmitter = Omni-VII with adjustable rise time
Undesired signal 700 Hz away, continuous “dits” at 30 wpm
Rise time of Omni-VII Strength of CW sidebands
Signal S9 + 40 -33 dBm Ref
3 msec S7 -83 dBm -50 dB
4 msec S6 -88 dBm
5 msec S6 -88 dBm
6 msec S5 -93 dBm 22 dB !
7 msec S4 -99 dBm
8 msec S4 -99 dBm
9 msec S4 -99 dBm
10 msec S3 -105 dBm -72 dB

## Slide 28
Spectrum of CW Signal on HP 3585A Analyzer
Rise Time 10 msec, “dits” at 30 WPM, Bandwidth -70 dB = +/- 450 Hz = 900 Hz

## Slide 29
Spectrum of CW Signal on HP 3585A Analyzer
Rise Time 3 msec, “dits” at 30 WPM, Bandwidth -70 dB = +/- 750 Hz = 1500 Hz

## Slide 30
Spectrum of CW Signal on HP 3585A Analyzer
Comparison of 3 msec vs 10 msec rise time
20 dB difference

## Slide 31
Leading edge of “dit” 3 & 10 msec

## Slide 32
How Many Poles Are Needed for a narrow CW roofing filter?
Orion II 600 Hz 4-pole filter is - 30 dB @ +/-700 Hz
Orion II 600 Hz 4-pole filter is – 50 dB @ +/-1200 Hz
A signal 2-kHz away is in the stop band of any filter.
Typical CW signal is +/- 700 Hz wide at –70 dB
The Orion II uses 4-pole roofing filters.
Sherwood has used a 6-pole filter for 32 years.
Elecraft uses both 5 and 8-pole filters.
I see no significant advantage of one choice over another.

## Slide 33
More Data on the K3
Roofing Filter Dynamic Range Noise Limited?
200 Hz 101 dB Yes
250 Hz 98 dB Mostly *
400 Hz 96 dB Mostly *
500 Hz 95 dB Mostly *
* Mostly = IMD audible, but noise predominates.

## Slide 34
From a Dynamic Range standpoint, reducing a strong adjacent signal 30 dB with a roofing filter is adequate. All the roofing filters from Ten-Tec, Elecraft, or Sherwood do the job. More poles have more insertion loss and cost more. Its a trade-off. Compared to a 15 kHz roofing filter, a 500 Hz CW roofing filters will pass about 3% of those signals on to the later stages of the radio. You likely cannot work a weak signal 1 kHz from an S9 +40 dB CW signal with any radio with the best roofing filter due to the transmitted bandwidth of the interfering signal.
Just the facts

## Slide 35: Conclusions
Contesters – DXers – Pileup operators need a good receiver for SSB and an even better receiver for CW.
The Sherwood 600-Hz CW roofing filter fixed the R-4C in 1976.
Ten-Tec Orion put that concept in a commercial design in 2003.
Elecraft K3 now also offers multiple roofing filters in 2008.

## Slide 36
25 years of up conversion radios have generally offered a 20 kHz dynamic range in the 90s but a 2 kHz close-in dynamic range in the 70s. Typical degradation of dynamic range within the up conversion filter bandwidth is 25 dB.
Now the buzz word is a 3-kHz roofing filter in up-conversion radios, though filter is often wider than spec.
IC-7800 3-kHz filter is 5+ kHz wide, 6-kHz is 11+ kHz
FT-2000 3-kHz filter is 7 kHz wide, and with my sample, it had 9 dB worse IMD than its 6 kHz filter.

## Slide 37
It is not possible to offer CW bandwidth Roofing Filters at VHF frequencies.
It all comes down to fractional bandwidth.
A 500-Hz filter at 5 MHz is like a 1-kHz filter at 10 MHz, or a 2 kHz filter at 20 MHz or a 4 kHz filter at 40 MHz & an 8 kHz filter at 80 MHz.
FTdx-9000 IF = 40 MHz, 3-kHz reasonable.
FT-2000 IF = 70 MHz, “3 kHz” = 7 kHz wide
The Orion II and the K3 roofing filters are in the 8 to 9 MHz range, similar to the R-4C at 5 MHz. Narrow filters are no problem here.
How Narrow Can a VHF Filter Be?

## Slide 38
Flex Radio
One of the few radios with no roofing filters at all is the Flex 5000A. It basically converts everything to baseband (typically 11 kHz) and filters it in DSP.
The Flex also performs very well with a completely different architecture, and with different tradeoffs.
You need $500 to $1000 computer and likely a $200 LCD monitor, but not a slew of $100 roofing filters.

## Slide 39
80 dB or better @ 2 kHz.
1976 Sherwood / Drake R-4C: 84 dB
2001 Ten-Tec Omni-VI+: 80 dB
2003 Icom IC-7800: 80 dB
2003 Ten-Tec Orion I: 93 dB
2005 Ten-Tec Orion II: 95 dB
2007 Flex 5000A: 96 dB
2007 Ten-Tec Omni-VII: 80 dB
2008 Elecraft K3: 95 to101 dB, depending on roofing and DSP filter bandwidth
What dynamic range is possible and needed for CW?

## Slide 40
Elecraft K2: 80 dB
Collins R-390A: 79 dB
Kenwood TS-850S: 77 dB
Icom Pro II / Pro III 75 dB
Collins 75S-3B/C: 72 dB
Kenwood TS-870S: 69 dB
Yaesu FT-2000: 63 dB
Icom IC-7000: 63 dB
Yaesu FT-One: 63 dB
Yaesu FT-101E: 59 dB
Drake R-4C Stock: 58 dB
Yaesu FT-757: 56 dB
Yaesu VR-5000: 49 dB
Other radios for comparison, 2 kHz dynamic range data

## Slide 41
Contest Fatigue & Audio Quality - The Forgotten Spec
Two transceivers made me tired in a long contest.
The audio was harsh on SSB and CW. Met OEM Spec
OEM spec = 2.5 watts @ 10% distortion = clipping
What makes audio harsh and fatiguing?
High Odd-Order Harmonics and / or IM Distortion
The ear / brain is very sensitive to these products.
Any product detector & audio amp will meet 10% spec
Thus the spec is meaningless.

## Slide 42
Harmonic Distortion of a Good Amp
Distortion < 0.3 % & sounds fine
-55 dB 2nd order
-68 dB 3rd order

## Slide 43
IM distortion of Good Amp
Distortion = 0.3 % & sounds fine
-53 dB 3rd order

## Slide 44
Not So Good Amp & Odd Order > Even
Distortion < 0.3 % but sounds bad
-65 dB 11th order

## Slide 45
Way too much IM Distortion
3% distortion but sounds terrible !
-40 dB 9th order IMD

## Slide 46
The Challenge = Get OEMs to Listen
In a 24 hour or 48 hour contest, you need every edge.
High Dynamic Range Receiver
Good Speech Processor on SSB
Big Tower and Good Antennas, etc.
But Your Brain Can Get “Fried” due to operator fatigue.
Bad audio can be a factor in that fatigue.

## Slide 47
Sherwood Engineering
http://www.sherwood-engineering.com
http://www.NC0B.com